## Slide 1: An overview of theory and execution
David M. Hamby, phd
April 6, 2022
VARSKIN+

## Slide 2: outline
From Classic VARSKIN to VARSKIN+
SkinDose Module
WoundDose Module
NeutronDose Module
EyeDose Module

## Slide 3: Classic Varskin to varskin+
VARSKIN (1987)
  originally designed to calculate radiation dose around a hot-particle point source in water from beta emitters; point and disk sources
SADDE (1989)
  new calculation of scaled absorbed dose distributions for betas emitted by nuclides that are not listed in the MIRD No. 7 publication
VARSKIN Mod 2 (1992)
  new routine to calculate scaled absorbed dose distributions for more nuclides and mixtures thereof; includes volumetric sources, layers of protective clothing, and a basic gamma dose estimator; backscatter correction applied; conversion and Auger electrons now considered along with beta emissions

## Slide 4: Classic Varskin to varskin+
VARSKIN 3 (2006)
  new Windows operating environment; syringe model added; new backscatter correction model; upgraded photon model; considers airgap and cover materials for electrons
VARSKIN 4 (2011)
  syringe model removed; enhanced photon dosimetry model to account for attenuation, charged particle buildup, and electron scatter; airgap and cover materials now considered for photons
VARSKIN 5 (2014)
  electron dosimetry model is enhanced and based on EGS Monte Carlo simulations rather than Berger’s point kernels; takes better account of electron scatter and energy loss in tissue, air, and volumetric sources; new backscatter correction model
VARSKIN 6 (2018)
  choice of including daughter emissions (full equilibrium); the ICRP 107 nuclide decay database is made available

## Slide 5: Classic Varskin to varskin+
VARSKIN+ (2021)
  created to house next version of VARSKIN, called SkinDose, and more!
V+ employs a new user interface written in Java and updated Fortran for physics calculations based on Fortran 2018
  computational speed has increased by as much as 25x
  alpha dosimetry has been added (SkinDose & WoundDose)
Additional computational modules added to VARSKIN+
  WoundDose
  NeutronDose
  EyeDose

## Slide 6: Skindose i.e., Classic Varskin
SkinDose

## Slide 7: outline
Basic Theory
  Photon dosimetry
  Electron dosimetry
  Alpha dosimetry
Examples
SkinDose

## Slide 8: Basic Theory
Photon Model
  point-kernel methodology numerically integrated over 300 dose point for each source point (up to 3,375)
  accounts for attenuation, charged particle buildup, and off-axis scattering
Electron Model
  point-kernel methodology numerically integrated over 60 dose points for each source point (512)
  accounts for air and source backscattering effects and source self-absorption
Alpha Model (new)
  calculated from the mass stopping power of particles as they pass through the dose averaging area
  assumed point source and limited definition of covers and airgaps given limited range of alphas
SkinDose

## Slide 9: SKINDOSE Photon dosimetry
The SKINDOSE photon dosimetry model considers:
  photon point-kernel methodology
  charge-particle buildup; material attenuation; off-axis scatter
  numerical integration of 300 dose kernels for each source kernel
  multiple geometries (point, disk, cylinder, sphere, slab, syringe)
  dose calculated to an averaging disk (0.01 to 100 cm2) at user-specified depth beneath skin surface
  variable dose averaging
    2D averaging areas (regulatory compliance)
    3D averaging volumes (detector simulation)
SkinDose

## Slide 10: Fundamentals: photon interactions
Photon interactions are random events, yet quantifiable
Photons generally interact with orbital electrons
Interaction probability is governed by:
  absorbing material (Z, electron density)
  photon energy (E)
… and is described by an interaction coefficient
Principal mechanisms of interaction include (by increasing energy):
  Thomson/Rayleigh scatter (no E transfer)
  photoelectric
  Compton scatter
  pair production
  photo-disintegration (very high E)
SkinDose

## Slide 11: Charged-Particle Equilibrium
Using a transfer coefficient, KERMA is easily estimated from photon flux
Dose, as a function of depth, must then be determined from a conversion of KERMA based on the buildup of electronic charge with tissue depth
Charged-Particle Equilibrium (CPE) is established once this charge buildup is complete
At shallow (e.g., SDE) depths, however, CPE is generally not yet established
SkinDose

## Slide 12: Elements of the photon dose calculation
Source Strength
Photon Energy
Geometric
Attenuation
Material
Attenuation
Probability of
Energy Transfer
Equilibrium
Fraction
Off-Axis
Adjustment
SkinDose

## Slide 13: Range-Energy Observations
Electrons lose energy via tortuous paths
Electron range (penetration depth) increases with increasing energy
Linear range is largely dependent on electron density of the absorber atoms
And, to a lesser degree, range is a function of Z
  result has practical implications for shielding
  density thickness (mg/cm2) is the best indicator of electron range
  important tissue depths  7, 100, 300, 1000 mg/cm2
SkinDose

## Slide 14: Electron Interactions
As energetic electrons pass through material, they transfer energy
  primarily via “soft” (Coulombic) collisions
  or “hard” (physical) collisions with orbital electrons
Energy loss is a function of KE & charge density
Energy loss can result in:
  excitation – characteristic X-rays
  ionization – scattered energetic electrons
  bremsstrahlung (>1 MeV electrons) – low-energy photons
Scattered electrons may produce additional ion pairs
  e.g., clusters, delta rays, further excitation/ionization
air
skin
Rb
SkinDose

## Slide 15: Electron Track Simulation
~90% Range
“Maximum” Range
Average Range
SkinDose

## Slide 16: Scaled Absorbed Dose Distributions
The factor F(r/r0,E) represents the SADD and is essentially a modified Bragg curve; shown for monoenergetic electrons of energy E, and for beta particles of distributed E, normalized over their maximum range, r0
r0
r
SkinDose

## Slide 17: Backscatter Correction Factors
SkinDose

## Slide 18: Alpha dosimetry
where is unit conversion constant, is the mass stopping power at the dose location, is the radiation weighting factor, is the source activity, is the alpha yield, is the exposure time, and is the total travel length of the alpha particle from point to receptor
Alpha dose (SDE) to receptor location I on an infinitely thin averaging disk is:

## Slide 19: Skindose sensitivities
Direct propagators – uncertainty in these parameters propagates completely through the model to the dose estimate (e.g., twice the exposure time will yield twice the dose)
Regulatory Defined Values – while these inputs can be manipulated in VARSKIN, the regulations call for dose averaged over 10 cm2 at a depth of 7mg/cm2, for example
Parametric Uncertainty – variations in these inputs will affect dose output; however, the effect is not as intuitive as compared to the direct propagators
Direct Propagators | Regulatory Defined Values | Parametric Uncertainty
Exposure time Source activity Distributed activity | Volume averaging depth Skin averaging area Skin thickness | Airgap thickness Cover thickness and density Source geometry
SkinDose

## Slide 20: Sensitive parameters – photon dose
Parameter | E < 20 keV | 20 keV - 500 keV | E > 500 keV
3D Geometry | LOW | LOW | LOW
3D Source volume | MODERATE | LOW | LOW
3D Source density (assumed to be air) | LOW | LOW | LOW
2D Source area* | LOW | LOW/MODERATE | LOW/MODERATE
Cover density | LOW | LOW | LOW
Cover thickness | LOW | MODERATE | MODERATE
Airgap thickness | LOW | MODERATE | MODERATE
SkinDose

## Slide 21: sensitive parameters – electron dose
Parameter | E < 200 keV | 200 keV – 2 MeV | E > 2 MeV
3D Geometry | LOW | LOW | LOW
3D Source volume | HIGH | HIGH/MODERATE | MODERATE
3D Source density | HIGH | HIGH/MODERATE | MODERATE
2D Source area (relative to avg area) | LOW | LOW/MODERATE | LOW/MODERATE
Cover density | MODERATE | MODERATE | LOW
Cover thickness | HIGH | LOW | LOW
Airgap thickness | LOW | MODERATE | MODERATE
SkinDose

## Slide 22: capabilities and limitations
Calculates dose equivalent for photon, electron, and alpha radiation for more than 1200 radionuclides
  uses either ICRP 38 or 107 decay data and accounts for decay products
Dose at depth can be averaged over an area from 0.01 cm2 to 100 cm2
Allows for an airgap of up to 20 cm between the source and the skin surface and for source covers
Source materials are defined by atomic number and density with geometries of:
  point and disk sources
  volumetric sources (i.e., spherical; cylindrical; slab; syringe)
GUI warns the user that an input value is out of range but continues with the calculation!
SkinDose

## Slide 23: EXAMPLE 1: Co-60 hot particle
A 1 µCi “speck” of Co-60 (activated metal) is found on a worker’s arm
Thought to be on the arm for the past hour
Using ICRP 107 decay data with Zeff of 27
No air gap and no cover material
Estimate the SDE to a 10 cm2 averaging area at a depth of 7 mg/cm2
SkinDose

## Slide 24
SkinDose

## Slide 25
1 micron
70 microns
SkinDose

## Slide 26
SkinDose

## Slide 27
SkinDose

## Slide 28
SkinDose

## Slide 29
SkinDose

## Slide 30
SkinDose

## Slide 31
SkinDose

## Slide 32
point source
SkinDose

## Slide 33: Example 2: Liquid radioactivity spilled on the arm (point)
Technician exposed to 1.85 MBq of 186Re for 4.5 hours
Start with the point-source geometry to determine order-of-magnitude, most conservative dose
Dose calculated at a depth of 7 mg/cm2 with 10 cm2 averaging:
1,300 mSv from electrons
2.1 mSv from photons
SkinDose

## Slide 34: Liquid radioactivity spilled on the arm (disk)
Now let’s work toward more realism
Assume the source takes the shape of a 50 cm2 spot directly on the skin (no air gap and no cover)
Therefore, we use the disk geometry with an 8 cm diameter
Dose calculated at a depth of 7 mg/cm2 with 10 cm2 averaging:
260 mSv from electrons
0.45 mSv from photons
SkinDose

## Slide 35: Liquid radioactivity spilled on a lab coat (disk)
Now assume the 50 cm2 spot is on top of a lab coat, which has a thickness of 0.04 cm and a density of 0.9 g/cm3
Again, we use the disk geometry with an 8 cm diameter, but now the lab coat material acts as a cover
Dose calculated at a depth of 7 mg/cm2 with 10 cm2 averaging:
90 mSv from electrons
0.37 mSv from photons
SkinDose

## Slide 36: Liquid radioactivity in the lab coat (cylinder)
For the most realistic assessment, we assume the 50 cm2 spot is soaked into the lab coat
This time we use the cylinder geometry, and the source is the coat itself
8 cm diameter, a 0.04 cm thickness, and a density of 0.9 g/cm3
Dose calculated at a depth of 7 mg/cm2 with 10 cm2 averaging:
160 mSv from electrons
0.42 mSv from photons
SkinDose

## Slide 37: Dose Summary
Geometry | Electron Dose (mSv) | Photon Dose (mSv)
Point on Skin | 1,300 | 2.1
Disk on Skin | 260 | 0.45
Disk above Coat | 90 | 0.37
Cylinder in Coat | 160 | 0.42
SkinDose
Bounding
Most realistic

## Slide 38: wounddose
WoundDose

## Slide 39: outline
Technical Basis and Theory
Overview of new WoundDose GUI
  Shallow dose equivalent
  Local dose equivalent
  CEDE and CODE (systemic)
Examples
WoundDose

## Slide 40: Basis for Wound Model Dosimetry
NCRP Report No. 156, “Development of a Biokinetic Model for Radionuclide-Contaminated Wounds and Procedures for Their Assessment, Dosimetry, and Treatment” (2007)
The wound model consists of three distinct dosimetry calculations:
  (1) Shallow dose Equivalent (@ 7 mg/cm2)
  (2) Local dose equivalent (to tissue)
  (3) organ/effective dose equivalent (systemic uptake)
Type of wound will determine applicable dose calculations
WoundDose

## Slide 41: General method
Designed for penetrating wounds where radioactive contamination has been forced under the skin surface
Consists of three distinct dosimetry calculations: (1) SDE; (2) local dose equivalent; and (3) committed organ/effective dose equivalent (systemic)
SDE
  Total dose at the shallow depth (7 mg cm-2 ) with an embedded wound source and dose area of 10 cm2
  Dose models same as SkinDose, except for retention class, abrasion thickness (for point source), and wound penetration depth inputs
Local Dose
  Dose equivalent to the tissue surrounding the contaminated wound volume
  Volume surrounding a point source at a given depth or volume surrounding the penetration depth of a line source
WoundDose

## Slide 42: General method
Systemic Dose
  The biokinetic model considers four uptake categories: (1) radionuclides in soluble form; (2) particulates, aggregates, and bound states; (3) colloid and intermediate states; and (4) fragments
  Movement of material from the wound and through the body to the bloodstream is characterized by the biokinetic model in NCRP 156
  Dose is estimated using tabulated internal dose coefficients for radionuclides (limited number) reaching the bloodstream via penetrating wounds
    for all seven solubility characteristics provided by the NCRP 156 model
    allows for custom biological half-life at wound site
WoundDose

## Slide 43: Historical wound experience
Industrial
  vast majority of contaminated wounds involved actinides
  > 90% occur in hands and arms, primarily fingers
  ~ 90% involve punctures and chemical burns
Military
  embedded U and Pu compounds/fragments
Medical
  needle sticks in radiopharmaceutical labs
  accidental injections of Thorotrast® (232Th)
WoundDose

## Slide 44: Intact Skin, Abrasions and Non-severe Burns
For contamination events involving less-severe wounds where the skin remains intact, is lightly abraded, or has been lightly burned, dose assessments can be conducted using WoundDose to estimate the SDE calculations in a manner like that of SkinDose (i.e., no activity gets in the bloodstream)
The shallow dose model is altered only by the removal of some or all of the protective dead layer of skin
NCRP 156 states the following …
  For contaminated wounds in which the skin is largely intact, [VARSKIN] dose calculations may be directly applicable. For embedded contamination, Berger’s point kernels may be integrated over the depth of interest
Previous versions of VARSKIN (before V5) for beta dosimetry were based on point kernels developed by Berger (1971). The more recent VARSKIN and SkinDose packages (V5.0 and later) have their foundation in Monte Carlo simulations using EGSnrc for electron dosimetry, but the methods are essentially the same.
  WoundDose draws on the shallow dose model of SkinDose
WoundDose

## Slide 45: Severe Burns, Lacerations and Penetrating Wounds
For penetrating wounds where radioactive contamination has been forced under the skin surface, WoundDose will calculate dose for electrons, photons, and alpha particles for all three dose outcomes:
(1) Shallow dose Equivalent (@ 7 mg/cm2)
  draws on SkinDose
(2) Local dose equivalent (to surrounding tissue)
  refers to a determination of the dose to tissue surrounding the contaminated wound
(3) Organ/effective dose equivalent (systemic uptake)
  committed systemic dosimetry for uptakes to the bloodstream
WoundDose

## Slide 46: Residence time
Calculations of shallow and local dose are conducted for the estimated time that the radioactive contamination remains at the wound site (e.g., residence time)
This residence time (t) is the time-integration of the retention function:
WoundDose

## Slide 47: Wound Residence time by Retention class
Class | Biological Half-life (d) | Biological Residence Time* (d) | Biological Residence Time (yr)
Weak | 0.40 | 0.58 | 
Moderate | 4.0 | 5.7 | 
Strong | 150 | 210 | 0.58
Avid | 560 | 810 | 2.2
Colloid | 760 | 1,100 | 3.0
Particle | 1,700 | 2,400 | 6.6
Fragment | 110,000 | 150,000 | 410**
*time integral of triple-exponential wound retention; derived from NCRP 156 Table 4.11
**50-year maximum
WoundDose

## Slide 48: Shallow Dose
In 10 CFR 20.1003, shallow skin dose is defined for external exposures and is to be determined at a basal-layer depth of 70 microns (7 mg/cm2; 0.007 cm; 70 microns) beneath the surface of the skin
  this depth is assumed to be appropriate for the determination of risk (~dead layer thickness)
The regulation in 10 CFR 20.1201 also requires that shallow skin dose be “averaged over the contiguous 10 square centimeters of skin receiving the highest exposure”
If an abrasion were to occur, in which a portion or all of the dead layer of skin were removed, the depth at which shallow dose is determined would be altered by the thickness of removed tissue (alive or dead)
WoundDose

## Slide 49: Shallow Dose
To estimate total dose at the shallow depth (70 microns) with an embedded wound source, the models of SkinDose are accessed, but with modified backscatter correction (full correction in current version)
In addition to the typical skin dosimetry inputs, the user would enter the thickness of any surface tissue that might have been removed by the wound, as well as the wound retention class (e.g., weak, moderate, strong), and an estimate of its penetration depth
WoundDose

## Slide 50: Shallow Dose
Point Source at Depth: In this case, the distance between source and skin averaging area is determined by the difference between source depth and the defined shallow depth (70 microns)
The user still has the option to select the depth at which dose is calculated, but 70 microns is the default
WoundDose
Air
Skin
dose averaging
area (at 70 mm)
point
source
SkinDose
Air
Skin
dose averaging
area (at 70 mm)
point
source
WoundDose

## Slide 51: Shallow Dose
Line Source Surface to Depth: In this instance, it is assumed that a puncture has occurred (e.g., contaminated screwdriver or a needle stick) and any remnant of contamination is evenly distributed along the puncture route
The shallow dose at 70 microns to a specified skin averaging area (10 cm2) is calculated under the assumption that the perpendicular line source begins at the surface, possibly penetrates the averaging area, and continues to the user-specified wound depth
The problem in this case requires the integration of dose over a series of point sources at depth, along the wound penetration line
Air
Skin
dose averaging
area (at 70 mm)
line
source
WoundDose

## Slide 52: Local dosE
Local wound dosimetry is straightforward … energy absorbed per unit mass
NCRP 156 states, “If the activity in the wound is known … dose calculations may be limited to the volume [mass] of tissue actually irradiated …”
But “irradiated mass” can be ambiguous
For radioactivity in the liver, the mass of liver is assumed to be uniformly irradiated
If radioactivity is localized in a tissue wound, the irradiated mass is that which absorbs energy
  i.e., a tissue sphere with radius equal to the range of the most penetrating particle
For example, 32P electrons have a range (95%) of about 0.54 cm in tissue i.e., rV = 6.7x10-1 g
whereas, 150Gd alphas have a range of about 18 microns in tissue i.e., rV = 2.4x10-8 g
WoundDose

## Slide 53: Local dosE
Dose for a 1 kBq point source of 32P (Eavg = 0.695 MeV): Local DE = 0.60 mSv/h
And a 1 kBq point source of 150Gd (Ea = 2.75 MeV): Local DE = 1.3 MSv/h
But a wound with both nuclides (i.e., using larger volume??): Local DE = 48 mSv/h
However, with a standard volume (1 cm3, r = 0.62 cm):
  1 kBq 32P Local DE = 0.4 mSv/h
  1 kBq 150Gd Local DE = 31.7 mSv/h
  1 kBq 150Gd + 1 kBq 32P Local DE = 32.1 mSv/h
All alpha and electron energy is assumed deposited within 1 cm3
  good assumption for 95% absorption until about Ee > 2 MeV
X
WoundDose

## Slide 54: Local Dose
For a point source, particle/photon emitted energy is assumed to be deposited in a standard spherical volume of 1 cm3 (radius = 0.62 cm). For a line source, the deposition volume is assumed to be a cylinder of radius 0.62 cm with hemispherical endcaps (NRCP 156).
WoundDose
Source geometry options:
cylindrical volume
along the line source
spherical volume
around the point source

## Slide 55: Local Dose
Electrons: For a point source beneath the skin surface, the local dose due to electrons is:
  where c handles unit conversion, Q is the activity initially introduced into the wound, is residence time, is unity for electrons, Y is electron emission yield, is average electron energy (considering all beta and electron emissions), ρ is tissue density, and is the absorption volume (1 cm3)
Alphas: The local dose due to alpha emissions is:
  where is 20 for alpha particles and is the energy of the ith alpha with yield
WoundDose

## Slide 56: Local Dose
Photons. The photon dose for an embedded point source is calculated for energy deposited in a surrounding 1 cm3 sphere, using:
  where w is unity for photons, and the fraction of photon energy deposited within a sphere of radius r (0.62 cm) around the source is:
  with and representing energy-specific linear absorption and attenuation coefficients in tissue, respectively
WoundDose

## Slide 57: Systemic Dose
The biokinetic model for radiologically contaminated wounds considers four uptake categories:
  radionuclides in soluble form (4 classes)
  colloids and intermediate states
  particulates, aggregates, and bound states
  fragments
Movement of material from the wound, through the body to the bloodstream is characterized by the biokinetic model in NCRP 156
WoundDose

## Slide 58: NCRP 156 systemic uptake model
Accidental Injection
Soluble
Fragment
Trapped Particles & Aggregates
Colloid & Intermediate State
Particles, Aggregates & Bound States
Blood
Lymph Nodes
WoundDose

## Slide 59: NCRP 156 systemic model default transfer rates
Transfer Rates (d-1) | Weak | Moderate | Strong | Avid | Colloids | Particles | Fragments
Soluble to blood | 45 | 45 | 0.67 | 7.0 | 0.5 | 100 | -
Soluble to CIS | 20 | 30 | 0.6 | 30 | 2.5 | - | -
CIS to soluble | 2.8 | 0.4 | 0.024 | 0.03 | 0.025 | - | -
CIS to PABS | 0.25 | 0.065 | 0.01 | 10 | 0.05 | - | -
CIS to lymph nodes | 0.00002 | 0.00002 | 0.00002 | 0.00002 | 0.002 | - | -
PABS to soluble | 0.08 | 0.02 | 0.0013 | 0.005 | 0.0015 | 0.0002 | -
PABS to lymph nodes | 0.00002 | 0.00002 | 0.00002 | 0.00002 | 0.0004 | 0.0036 | 0.004
PABS to TPA | - | - | - | - | - | 0.04 | 0.7
TPA to PABS | - | - | - | - | - | 0.0036 | 0.0005
Lymph nodes to blood | - | - | - | - | 0.03 | 0.0006 | 0.03
Fragment to soluble | - | - | - | - | - | - | -
Fragment to PABS | - | - | - | - | - | - | 0.008
WoundDose

## Slide 60: Wound dose coefficients for systemic uptake
For 38 radionuclides, Toohey et al. (2014)* contains tables of:
  compartment transfer rates by retention class
  CODE coefficients by retention class
  CEDE coefficients by retention class
  and derived regulatory guides and clinical decision guides for a subset of radionuclides
For example, each nuclide (241Am in this case) has 7 effective dose coefficients [x10-4 Sv/Bq]:
  Soluble 3.97 (weak) 3.96 (moderate) 3.91 (strong) 3.79 (avid)
  Insoluble 3.80 (colloid) 2.23 (particle) 0.141 (fragment)
*Toohey, R.E; Bertelli, L.; Sugarman, S.L.; Wiley, A.L.; Christensen, D.M. Dose coefficients for intakes of radionuclides via contaminated wounds. Oak Ridge Institute for Science and Education. US DOE Contract No. DE-AC05-06OR23100. Oak Ridge, TN; Ver. 2, August 2014.
WoundDose

## Slide 61: capabilities and limitations
Considers all radionuclides in ICRP 38 and 107
Geometry limited to point source (hot particle) and line source (uniform contamination)
7 wound retention classes (plus custom biological half-life)
User defined abrasion depth, injury penetration depth, and shallow dose depth
Separate outputs for SDE, local DE, and systemic CEDE
Systemic dose is limited (at the moment) to select radionuclides with available dose coefficients
WoundDose

## Slide 62: Example 1: Embedded cobalt-60
Assume a 1 kBq Co-60 (ICRP 107) point source
5 mm injury depth
1 mm abrasion depth
Examine “colloid”, “particle” and “fragment” retention classes
SDE to a 10 cm2 averaging area at a depth of 7 mg cm-2
Local DE to a 1 cm3 sphere around the point source
System CEDE
WoundDose

## Slide 63
WoundDose

## Slide 64: Cobalt-60 wound dosimetry for 3 retention classes
Retention Class | Shallow Electron Dose (mSv) | Shallow Photon Dose (mSv) | Local Electron Dose (mSv) | Local Photon Dose (mSv) | CEDE (mSv)
Colloid | 0.0 | 39 | 1,000 | 480 | 0.014
Particle | 0.0 | 60 | 1,700 | 800 | 0.0061
Fragment | 0.0 | 100 | 3,600 | 1,700 | 0.00025
WoundDose

## Slide 65: Example 2: Tc-99m Needle Stick
A nuclear medicine technologist sustains a needlestick to the index finger
  2.2 MBq of Tc-99m is assumed injected to a depth of 2 mm
WoundDose will be used to estimate SDE, local DE, and systemic CEDE
We’re not confident with our knowledge of 99mTc retention (at the wound site), therefore we will calculate dose according to the “weak”, “moderate” and “strong” retention models
We will estimate dose for both point- and line-source geometries
SDE will be averaged over a 1 cm2 area (because the stick was to the index finger)
WoundDose

## Slide 66
WoundDose

## Slide 67: Tc-99M Needle-stick dosimetry summary
Geometry | Retention Class | Shallow Electron Dose (mSv) | Shallow Photon Dose (mSv) | Local Electron Dose (mSv) | Local Photon Dose (mSv) | CEDE (mSv)
Point | Weak | 0.0 | 11 | 860 | 16 | 0.033
 | Moderate | 0.0 | 15 | 1,300 | 25 | 0.026
 | Strong | 0.0 | 16 | 1,400 | 26 | 0.0071
Line | Weak | 310 | 23 | 690 | 13 | 0.033
 | Moderate | 410 | 31 | 1,100 | 20 | 0.026
 | Strong | 420 | 32 | 1,100 | 21 | 0.0071
WoundDose

## Slide 68: Example 3: Pu-238 puncture wound
An employee experiences a 1-mm deep puncture wound (from a braided steel cable) to the finger
Determined that 392 Bq of Pu-238 was initially injected into the wound
Excision and chelation therapy resulted in the remove of 322 Bq, for a net intake of 70 Bq
The “Avid” retention model was determined to be appropriate
Dose will be estimated for point- and line-source geometries
WoundDose

## Slide 69
WoundDose

## Slide 70: Pu-238 puncture Wound dosimetry summary
Wound Activity (Bq) | Geometry | Shallow Electron Dose (Sv) | Shallow Photon Dose (Sv) | Shallow Alpha Dose (Sv) | Local Electron Dose (Sv) | Local Photon Dose (Sv) | Local Alpha Dose (Sv) | CEDE* (Sv) | CODE (Sv)
392 | Point | 0.0 | 0.0049 | 0.0 | 4.2 | 0.0035 | 480 | 0.16 | 5.4
 | Line | 0.57 | 0.012 | 6,500 | 3.8 | 0.0031 | 430 | 0.16 | 5.4
70 | Point | 0.0 | 0.00088 | 0.0 | 0.76 | 0.00062 | 85 | 0.029 | 0.97
 | Line | 0.10 | 0.0021 | 1,200 | 0.68 | 0.00056 | 77 | 0.029 | 0.97
*Radiation safety staff determined a pre-treatment CEDE of 0.1638 Sv and a post-treatment CEDE of 0.0296 Sv
WoundDose

## Slide 71: Neutrondose
NeutronDose

## Slide 72: outline
Basic theory
  scatter (elastic and inelastic)
  radiative capture
  absorption reactions
General dosimetry equations
KERMA response
Charged particle equilibrium
Neutron sources
Examples
NeutronDose

## Slide 73: Basic Neutron Dosimetry
Consideration is made for neutron interactions from energies spanning thermal to fast (up to 20 MeV)
  set of KERMA values can be generated using neutron interaction equations
  depth-dose equations can then be applied to these values for an estimate of neutron dose at a specific depth
  this is especially important for incident neutrons above 1 MeV where charged particle KERMA is not equivalent to dose at shallow depths
Principle concern of occupational radiation exposure is carcinogenesis in mitotically active cells (stratum basale)
  ICRU 4-component soft tissue
How radiation interacts with matter depends on its type, energy, and elemental composition of the medium
  similar to photons, neutrons are indirectly ionizing
  they interact with the nucleus of an atom, however, rather than its atomic orbitals
NeutronDose

## Slide 74: KERMA
Neutron KERMA represents the kinetic energy transferred from neutrons to charged particles in an absorbing medium
The type and abundance of reactions that could occur depends on the incident neutron energy, elemental composition of tissue, and the various reaction cross sections:
where Nj is the number of atoms per unit mass of element j defined by the ICRU 44 elemental composition of soft tissue
ϵij (E) is the energy transferred to charged particles as kinetic for nuclide j and interaction I
and σij (E) is the microscopic cross section for a given reaction
NeutronDose

## Slide 75: KERMA
The neutron fluence after attenuation through thickness d of tissue is:
The total macroscopic cross section (Σt) describes the probability of any interaction within that medium and can be calculated by:
Unlike KERMA, absorbed dose requires consideration of energy transferred specifically to ionization by secondary charged particles within the dose volume. However, these two values are closely related such that determination of KERMA can be used to approximate dose, with the appropriate application of fractional CPE when they are not equal
NeutronDose

## Slide 76: kerma
Pertinent cross sections were gathered from the Evaluated Nuclear Data File (ENDF) to build neutron KERMA in tissue
Each of the possible neutron reactions was evaluated individually before summation to determine the total KERMA at a given incident neutron energy
NeutronDose

## Slide 77: KERMA
NeutronDose

## Slide 78: Response Function by Mechanism
fCPE = 1
NeutronDose

## Slide 79: Neutron Dosimetry: Scatter
Dominant at higher neutron energies
Neutrons transfer kinetic energy by direct collision with the atomic nuclei that make up tissue (H, C, N, and O)
The majority of energy (>85%) deposited by scatter occurs due to neutron collisions with hydrogen nuclei
Collisions with oxygen nuclei account for as much as 15% of scatter dose above ~1 MeV
Element | Atomic Fraction (%) | Nj (atoms kg-1)
Hydrogen | 10.12 | 
Carbon | 11.10 | 
Nitrogen | 2.60 | 
Oxygen | 76.18 | 
Element | Atomic Fraction (%) | Nj (atoms kg-1)
Hydrogen | 10.12 | 
Carbon | 11.10 | 
Nitrogen | 2.60 | 
Oxygen | 76.18 | 
NeutronDose

## Slide 80: Neutron Dosimetry: Elastic Scatter
An incident neutron with kinetic energy, E, collides with a target nucleus of mass, A, that recoils at some angle with respect to the incident direction of the neutron
Since the nucleus does not enter an excited state, the average energy transferred to charged particles is given by:
Isotropic scatter is assumed in the center-of-mass system so that
NeutronDose

## Slide 81: Neutron Dosimetry: Inelastic scatter
Inelastic scatter is a threshold reaction, requiring the incident neutron to carry enough energy to excite the nucleus to a specific excited state, Q
Average energy transferred to charged particles:
Isotropic scatter is still assumed ()
NeutronDose

## Slide 82: Neutron Dosimetry: Scatter
, the fast-neutron equivalent dose from elastic (and inelastic) scatter with element i:
where the value of , the fractional energy transferred to kinetic of the recoil proton for element i during elastic scatter:
Inelastic scatter events result in the excitation energy being carried away from the dosimetric space by photons of varying energy
NeutronDose

## Slide 83: Neutron Dosimetry: Scatter
fCPE = 1
NeutronDose

## Slide 84: Neutron Dosimetry: Radiative Capture
Target nucleus of mass A absorbs an incident neutron with kinetic energy E, briefly forming an excited atom A’.
The atom de-excites through the emission of a photon with energy Eγ that may deposit energy elsewhere or leave the tissue medium
Conservation of momentum dictates an energy balance between the recoil nucleus and photon emission:
NeutronDose

## Slide 85: Neutron Dosimetry: absorption Reactions
A compound nucleus is briefly formed before the emission of a charged particle
Subsequent nucleus may be left in an excited state depending on the incident neutron energy
Energy transferred depends on the incident energy of the neutron, En, the mass difference, Q, and the level of the excited state, Es:
NeutronDose

## Slide 86: Neutron Dosimetry: Capture/Absorption
Dominant at low (thermal) energies
Two significant capture/absorption interactions emerge:
  1H(n,g)2H Q = 2.224 MeV
  14N(n,p)14C Q = 0.626 MeV
Capture results in the emission of a high-energy photon to be absorbed elsewhere
  this mechanism may be insignificant when evaluating shallow dose equivalent
  but the generation of photons in shielding materials can be significant (not currently handled by NeutronDose)
Absorption in tissue results in an energetic proton and carbon recoil, the combined energy of which is deposited within the range of the proton
  i.e., about 10 microns in tissue
NeutronDose

## Slide 87: Neutron Dosimetry: Capture/Absorption
𝐻(𝑑), the equivalent dose at depth, d, due to neutron capture by 1H or absorption by 14N is calculated using:
where N is the atomic mass density of 1H or 14N (atoms kg-1)
Q is the reaction energy (MeV), AF is the fraction of energy absorbed locally in tissue
𝑤𝑅 (𝐸) is the radiation weighting factor (Sv/Gy)
𝜎(𝐸) is the energy-dependent cross section (cm2 atom-1)
𝑓𝐶𝑃𝐸 (𝑑,𝐸) accounts for fractional charged particle equilibrium
and Φ′(𝑑,𝐸) is the neutron fluence at depth (cm-2 MeV-1)
NeutronDose

## Slide 88: Neutron Dosimetry
Equivalent dose for interactions by neutrons of energy E, with element i, by mechanism j, at depth d:
where:
= energy conversion [J MeV-1];
= Avogadro's number [atoms mol-1];
= atom weight-fraction;
= atomic weight [kg mol-1];
= interaction energy absorbed locally [MeV];
= radiation weighting factor [Sv Gy-1];
= interaction cross section [cm2 atom-1];
= fractional charged particle equilibrium; and
= neutron fluence at depth [cm-2 MeV-1].
Ai is the mass number of element i;
E is the incident neutron energy [MeV];
Qi is the reaction energy [MeV];
and AFi is the absorbed fraction.
NeutronDose

## Slide 89: Fractional Charged Particle equilibrium
Neutron KERMA is equivalent to dose where charged particle equilibrium is established
CPE is said to exist if for every charged particle leaving a volume an identical enters
In the buildup region each subsequent volume of interest approaches equilibrium
For shallow dosimetry, however, the CPE approximation is not an accurate reflection of dose
Equilibrium fraction by incident neutron energy was modeled with MCNP
NeutronDose

## Slide 90: Neutron fCPE in Tissue
NeutronDose

## Slide 91: Neutron Sources
The NeutronDose module provides dosimetry for six different source types:
  - spontaneous fission - photoneutrons (g,n)
  - neutron-induced fission - monoenergetic neutrons
  - alpha-reaction neutrons (a,n) - user-uploaded custom energy distributions
NeutronDose

## Slide 92: Neutron Sources
Both spontaneous fission and neutron-induced fission sources use the Watt fission spectrum equation:
The values A and B are taken from ICRP 107 for spontaneous fission sources, and from Shultis and Faw (2000) for neutron-induced fission as a function of incident neutron energy, E, up to a maximum of 10 MeV
The leading coefficients, Br and , represent the branching ratio and average number of neutrons produced per fission for spontaneous fission events
Fissile or fissionable nuclides:
  233U, 235U, 238U, 239Pu, 232Th
Spontaneous fission for nuclides of these elements:
  U, Np, Pu, Am, Cm, Bk, Cf, Es, Fm
NeutronDose

## Slide 93: Neutron Sources
Source | Reaction | Avg. Neutron Energy (MeV) | Neutron yield per alpha
Am-241 / 10B | 10B(a,n)13N | 3.0 | 1.39E-5
Am-241 / 9Be | 9Be(a,n)12C | 4.4 | 7.22E-5
Am-241 / 19F | 19F(a,n)22Na | 1.5 | 4.17E-6
Cm-242 / 9Be | 9Be(a,n)12C | 4.1 | 9.17E-5
Pu-239 / 9Be | 9Be(a,n)12C | 4.6 | 4.70E-5
Pu-239 / 13C | 13C(a,n)16O | 4.2 | 3.17E-6
Source | Reaction | Avg. Neutron Energy (MeV) | Number of photons per decay | Neutron yield per decay*
As-76 / 9Be | 9Be(g,n)8Be | 0.108; 0.382 | 0.010 | 1.9E-6
Ga-72 / 9Be | 9Be(g,n)8Be | 0.173; 0.476; 0.733; 0.748 | 0.0517 | 1.4E-6
Ga-72 / D2O | 2H(g,n)1H | 0.131; 0.139 | 0.205 | 1.6E-6
In-116m / 9Be | 9Be(g,n)8Be | 0.396 | 0.154 | 2.2E-7
La-140 / 9Be | 9Be(g,n)8Be | 0.761 | 0.034 | 8.0E-8
La-140 / D2O | 2H(g,n)1H | 0.146 | 0.034 | 2.0E-7
Mn-56 / 9Be | 9Be(g,n)8Be | 0.128; 0.397; 0.761 | 0.425 | 7.8E-7
Mn-56 / D2O | 2H(g,n)1H | 0.146; 0.214 | 0.017 | 8.0E-8
Na-24 / 9Be | 9Be(g,n)8Be | 0.967 | 1.0 | 3.5E-6
Na-24 / D2O | 2H(g,n)1H | 0.262 | 1.0 | 7.3E-6
Sb-124 / 9Be | 9Be(g,n)8Be | 0.022; 0.378 | 0.547 | 5.1E-6
Y-88 / 9Be | 9Be(g,n)8Be | 0.151; 0.949 | 0.999 | 2.7E-6
Y-88 / D2O | 2H(g,n)1H | 0.252 | 0.006 | 8.0E-8
Characteristics of Alpha Reaction Sources Provided in V+ (Lorch 1973)
*neutrons emitted from 1 g of Be or D2O placed 1-cm away
NeutronDose
Characteristics of Photoneutron Sources Provided in V+ (Shultis & Faw 2000)

## Slide 94: Capabilities and current limitations
Neutron sources include
  spontaneous fission
  neutron-induced fission
  alpha reaction neutrons (a,n)
  photoneutrons (g,n)
  a monoenergetic neutron
  a user-uploaded custom energy distribution
User inputs depend on source selection
  inputs are used to define an orthogonal beam at the skin layer
Source geometries not allowed; all assumed to be orthogonal beams
No shielding or source covers
On contact sources not permitted at this time!
NeutronDose

## Slide 95: EXAMPLE 1: exposure to a PuBe source
Assume (a,n) reaction with Pu-239/Be-9 source
At a distance of 1 m and source strength of 1 Ci
Shallow dose at 7 mg/cm2 for a 1-hr exposure time
NeutronDose

## Slide 96: Example 2: exposure to a Cf-252 laboratory source
A student is to conduct a laboratory experiment requiring an 80-minute exposure to Cf-252 at 5 meters
Cf-252 has …
  an intrinsic specific activity of 19.86 TBq/g
  fission neutron emissions from zero to 13 MeV, with a mean of 2.3 MeV and a most probable energy of 1 MeV
This source had a mass of 1 gram 500 days prior to the experiment
Its current activity is therefore 13,860 MBq
Calculate SDE and dose at depth of 10 cm
NeutronDose

## Slide 97: Cf-252 exposure
NeutronDose

## Slide 98: Example 3: neutron dose rate from SbBe source
Sb-124 mixed with beryllium provides a photoneutron source
Results in two monoenergetic neutrons of about 22 and 380 keV
NeutronDose calculates a dose rate factor of 5.0 pSv m2 h-1 MBq-1
NeutronDose

## Slide 99: SbBe neutron dose rate
Alternatively, we can assume a point source with negligible self-absorption and use a neutron emission yield from the literature of 5.1x10-6 n/dis
… to determine a fluence factor (at 1 meter) of 0.14 n/cm2 per hour per MBq
Then, using the monoenergetic feature we can estimate the dose rate factor for each of the two monoenergetic neutrons (along with their related photon emission yields):
NeutronDose

## Slide 100: eyedose
EyeDose

## Slide 101: outline
Regulatory Basis
Early estimates with VARSKIN
Basic Structure
  photons
  electrons
  protective glasses
  off-axis corrections
V&V
Limitations
Examples
EyeDose

## Slide 102: Sensitivity by Structure
In order of decreasing sensitivity (Rohrschneider, 1929)
  Lens
  Conjunctiva
  Cornea
  Uvea
  Retina
  Optic Nerve
Assumption: Protect the lens and protect the eye
EyeDose

## Slide 103: Regulatory basis for eyedose
In the United States from 10 CFR 20.1201 (1991):
  150 mSv/yr
Internationally from ICRP 118 (2012):
  20 mSv/yr averaged over 5 consecutive years, not to exceed 50 mSv in any single year
Many nations adopted the ICRP recommendations, causing a renewed interest in eye dosimetry
  some RAMP users wanted to use the VARSKIN code to estimate eye dose
EyeDose

## Slide 104: Prior to Eyedose
We compared VARSKIN 5.3 to Monte Carlo simulation (MCNP6)
Using a simplified eye model with cornea, lens, and surrounding tissue all assumed to be of unit density
  to be closest to VARSKIN assumptions
Point sources located along centerline from contact to 20 cm
Dose estimated per incident electron
  to normalize for geometry
  cross-sectional area of 1 cm2 with 20 mm thickness, centered at a depth of 3 mm
Surrounding tissue
Lens
Cornea
EyeDose

## Slide 105: Source on Contact
*
VARSKIN underestimates by at least 10%
EyeDose

## Slide 106: with Air gap
*
*
5 1
EyeDose

## Slide 107: 20 10
*
*
EyeDose

## Slide 108: 1 cm Gap with Plastic
*
1cm
EyeDose

## Slide 109: 2 cm Gap with Plastic
*
2cm
EyeDose

## Slide 110: Eyedose model
Driven by a set of deterministic equations developed from a vast array of probabilistic simulations (MCNP)
  simulations of monoenergetic photons and electrons originating at varying distances from a stylized eye model
  source is assumed to be an infinitely small, isotropic point source located on the geometric axis
  dose calculated to the lens of the eye
Accounts for particle type, energy, source emission rate, and protective eyewear for:
  photon energies from 7 keV to 11 MeV
  electron energies from 100 keV to 11 MeV
  distances from 0 to 20 meters
Nuclide emissions (ICRP 38 and 107 data) are incorporated into the model
  as well as a placeholder for incorporation of emissions from X-ray machines (future project)
EyeDose

## Slide 111: Eye Geometry
The source in EyeDose is modeled as a monoenergetic, isotropic point source of energy E
The source is located on the geometric axis of the eye and the distance between the surface of the eyeball and the source is labeled r
Photons and electrons are modeled as they interact with structures of the eyeball
Bremsstrahlung created in the eyeball is incorporated into the dose calculation
EyeDose

## Slide 112: Photon Dosimetry
EyeDose

## Slide 113: Electron dosimetry
This new path opens at around r = 0.3 cm. The electron rays radiating from the source can be considered parallel at about 10 cm, at which point both the bremsstrahlung and direct contribution obey the inverse square law.
EyeDose

## Slide 114: Shielded vs Unshielded Dose
Protective glass thickness of 2 mm placed 1.25 cm from the cornea’s surface
Bremsstrahlung created in the safety glasses is incorporated into the dose calculation
EyeDose
1.25 cm

## Slide 115: Total Dose
In the presence of discrete energy particles (e.g., Auger electrons, characteristic X rays or gamma rays) and continuous energy spectra (e.g., beta radiation or X-ray machines), total dose is given by:
EyeDose

## Slide 116: Off-axis source
EyeDose

## Slide 117: Verification and validation - photons
EyeDose
Unshielded
Shielded

## Slide 118: Verification and validation - electrons
EyeDose
Unshielded
Shielded

## Slide 119: Current Limitations
Cannot adjust eye-glass parameters – built directly into the model (0.75 mm lead equivalent at 125 kVp)
Assumes the eyeball is centered on-axis for the entire exposure
  sensitivity study shows dependency on off-axis angle and energy
  difference between the on-axis and off-axis dose is within about 15% for θ < 20°
HOWEVER, the model accurately accounts for the curvature of the eye, the curvature of the lens, and the varying densities of the tissues of the eye and is a significant upgrade over using SkinDose to model a similar configuration
EyeDose

## Slide 120: Example 1: dose rate to the lens from Co-60
A person is exposed to a 37 MBq Co-60 source at 2.5 meters
What is the dose equivalent to the lens?
A back-of-the-envelope estimate to a small tissue volume is:
Now, we’ll use EyeDose (in two configurations) for the same calculation …
EyeDose

## Slide 121
EyeDose

## Slide 122: Example 2: exposure to sr-90
A technician is exposed to an “old” 2.3 mCi Sr-90 source with negligible encapsulation
What is the dose equivalent rate delivered to the lens of the eye at 30 cm?
What is the effect on dose from wearing 2-mm thick leaded glasses?
Nuclide | Geometry | Electron Lens Dose (mrem/h) | Shielding Effectiveness Factor
Sr-90 | Unshielded | 0.00025 | 6
 | Shielded | 0.000040 | 
Y-90 | Unshielded | 210 | 4,000
 | Shielded | 0.053 | 
EyeDose

## Slide 123: Effectiveness of leaded glasses
EyeDose

## Slide 124
QUESTIONS
DISCUSSION