## Slide 1: Overview of MACCS Status and Development – October 2023
AJ Nosek, PhD
US Nuclear Regulatory Commission (NRC)
2023 Fall RAMP Users’ Group Meeting October 23–27, 2023 Rockville, MD

## Slide 2: Outline
MACCS Code Overview
MACCS Calculational Models
  Atmospheric Dispersion
  Dosimetry
  Protective Actions
  Social and Economic Impacts
  Radiogenic Health Effects

## Slide 3: MACCS Code Overview: Purpose
The purpose of MACCS is to simulate and understand the public consequences of severe nuclear accidents.
Created by Sandia to support NRC research and regulatory applications
  Origins go back to the mid-1970s
MACCS is typically used for prospective analyses, e.g.,
  Probabilistic risk assessments (NUREG-1150 and NRC’s Level 3 PRA)
  Probabilistic consequence assessments (SOARCA)
  Consequence assessments for license and license renewal of nuclear facilities (support for NEPA analyses)
  Cost-benefit analyses (support for regulatory / backfit analyses)
  Research projects to inform emergency preparedness
MACCS is very versatile with a large set of user inputs
MACCS can quickly run thousands of Monte Carlo simulations for PRA applications
  Large set of weather trials (hundreds or thousands)
  Significant set of source term categories (ten or twenty) plus additional sensitivity studies

## Slide 4: MACCS Code Overview
MACCS belongs to the Cooperative Severe Accident Research Program (CSARP)
MACCS support codes include:
  WinMACCS
  MelMACCS
  SecPop
  MACCS-HYSPLIT Tools
  AniMACCS
Instructions for requesting the MACCS code and MACCS-related documents can be found at: https://maccs.sandia.gov/
NRC Cooperative Programs | Research Areas
Code Applications and Maintenance Program (CAMP) | Thermal Hydraulics
Cooperative Severe Accident Research Program (CSARP) | Severe Accidents
Radiation Protection Computer Code Analysis and Maintenance Program (RAMP) | Radiation Protection
MACCS Users by Country

## Slide 5: Overview: MACCS / RASCAL
 | MACCS | RASCAL
Inputs | Hundreds | <20
Input time | Hours to Days | <10 min
Run time | Minutes to Days | <5 min
Source Term | External Input | Included (Simplistic)
ATD Models | Y | Y
Weather | Sampled Historic Obs | Live Weather
Dose Calculations | Y | Y
Protective Actions | Credited | Not Credited
Health Effects | Y | N
Economic Effects | Y | N

## Slide 6: Overview: Phenomena Treated by MACCS
Emergency response
  Sheltering
  Evacuation
  Potassium iodide (KI) ingestion
  Relocation
Long-term protective actions
  Decontamination
  Temporary or permanent interdiction of property
  Crop disposal
Economic losses
  Evacuation and relocation per diem costs
  Long-term relocation cost
  Decontamination costs
  Loss of property use
  Depreciation during interdiction
  Property value for permanent interdiction
Radiogenic health effects
  Early health effects
  Cancer incidence / fatalities
Representation of source term
Atmospheric dispersion
  Statistical sampling of archived weather data
  Wet and dry deposition
Dose exposure pathways
  Inhalation
  Cloudshine
  Groundshine
  Resuspension
  Ingestion
  Skin deposition
Notes: Source term – imported as a file from MELCOR or similar application, or input directly into MACCS itself by specifying the release characteristics. Magnitude and timing, to include buoyancy (heat), height, initial timing, release rate by radionuclide by chemical group, particle size distribution by chemical group…items like that to characterize your release.
Models Atmospheric transport and dispersion – weather is a key part of that – options for statistical sampling of your weather data
(120 hour, bin sampling)
Deposition – deposited on the ground, or washed out by interactions with clouds or rain.
Exposure pathways – and ultimately the biological impacts and resulting risks
Broken down into multiple time domains:
Emergency – sheltering, biological impacts and potential shielding effects
Evacuation – speed and timing of evacuation for example. You can also modify this for certain groups of people, or modify speeds (weather)
Potassium Iodine Ingestion –
Relocation
Long Term effects:
Impacts on the land – work associated with decontaminating land, possible interdition, and crop disposal
Economic Losses:
Mentioned biological impacts, but a key part of MACCS is also calculating economic impacts to have a full picture of the risk.

## Slide 7: Overview: Progression of a MACCS Calculation
Outputs
Dosimetry
Health
Effects
Costs
Dose
Coefficients
Population
And Site Data
EARLY
Data
CHRONC
Data
Source Terms
Weather Data
ATMOS Data
Plume Rise
Transport and Diffusion
Deposition
ATMOS
EARLY / CHRONC
Protective Actions
Notes: ATMOS: Atmospheric transport in early phase
EARLY: Dosimetry, protective actions, and health effects from early phase.
- Early phase: Up to 40 days, usually one week.
CHRONC: Dosimetry, protective actions, and health effects from intermediate and long-term phases; Costs in all phases
- Intermediate phase: 0 to 30 years, usually zero or one year.
- Long-term phase: Exposure period depends on the pathway. EXPTIM up to 317 years, usually 30 or 50 years.

## Slide 8: Overview: MACCS Code Modules
ATMOS
  Estimates transient air and ground concentrations
  Option for Gaussian Plume Segment or Lagrangian Particle models
EARLY
  Treats emergency phase (up to 40 days, usually one week)
  Estimates projected doses from plume passage and ground contamination
  Models cohort-specific emergency response actions
  Estimates accumulated doses and health effects to cohorts
CHRONC
  Treats intermediate phase (up to 30 years, usually zero or one year)
  Treats long-term phase (up to 300 years, usually 50 years)
  Estimates projected doses from ground contamination
  Models long-term protective actions (i.e., relocation / property interdiction, food interdiction, decontamination, and condemnation)
  Estimates accumulated doses and health effects
  Estimates economic losses, land contamination, displaced individuals, and other societal impacts.

## Slide 9: Overview: MACCS Outputs
Output Name | ATMOS | EARLY | CHRONC
Type 0: Atmospheric Results for Specified Downwind Distances | X |  | 
Type 1: Health Effect Cases |  | X | X
Type 2: Early Fatality Distance |  | X | 
Type 3: Population Exceeding Early Dose Threshold |  | X | 
Type 4: Average Individual Risk |  | X | X
Type 5: Population Dose |  | X | X
Type 6: Centerline Dose |  | X | X
Type 7: Centerline Risk |  | X | X
Type 8: Population-Weighted Individual Risk |  | X | X
Type A: Peak Dose for Specified Distances |  | X | X
Type B: Peak Dose for Specified Spatial Elements |  | X | X
Type C: Land Area Exceeding Dose |  | X | 
Type D: Land Area Exceeding Concentration |  | X | 
Type E: Population Movement Across Radius |  | X | 
Type 9: Breakdown of Long-term Population Dose |  |  | X
Type 10: Economic Cost Measures |  |  | X
Type 11: Maximum Distance for Protective Actions |  |  | X
Type 12: Impacted Area / Population |  |  | X
Type 13: Maximum Annual Food Ingestion Dose |  |  | X
Type 14: Evacuated and Relocated Population |  |  | X
Notes: If you don’t run CHRONC, the outputs only contain early phase results. Also, even when you do run CHRONC, certain outputs do not include food and water ingestion. To include all MACCS dose exposure pathways, use Type 1 and 5 outputs.

## Slide 10: Overview: Spatial Grid
Calculations are performed on a radial polar grid
The user specifies the number of compass sectors and radial intervals, and the outer distance of each radial interval
MACCS calculates results for each spatial element
Example of MACCS polar coordinate grid with 16 sectors and 3 radial divisions. (reproduced from Fig. 2-1 of NUREG/CR-6613 Vol. 1

## Slide 11: Overview: Time-Dependent Calculations
Network evacuation scheme
The timing of protective actions affects consequences
Example: Figure below shows groundshine dose accumulation during the emergency phase

## Slide 12: Atmospheric Dispersion
Gaussian approach:
  Gaussian plume equations with dispersion parameters
  Plume nearfield effects (building wake and meander)
  Boundary layer constraint
  Wet and dry deposition
  Off-centerline correction factors
MACCS / HYSPLIT approach:
  HYSPLIT (HYbrid Single-Particle Lagrangian Integrated Trajectory) is a code for computing complex dispersion and deposition simulations
  HYSPLIT is executed independently of MACCS
  HyGridConvert is used to convert air and ground concentrations from HYSPLIT to MACCS spatial grid
Factors common to both:
  Weather sampling routine
  Plume rise height calculation
  Radioactive decay and ingrowth
Figure from HYSPLIT User’s Guide (2022, p. 110)
Notes: ATD to calculate air and ground concentrations

## Slide 13: Atmospheric Dispersion: Gaussian Transport Model
The plume segment direction is based on observed wind direction at time of release.​
After release, plume segments do not change direction.​
After release, plume segment dispersion changes with observed changes in weather​
  Plume speed changes with windspeed​
  Plume diffusion rate changes with stability class​
  Wet deposition rate changes with rain rate​
Gaussian Plume Segments

## Slide 14: Atmospheric Dispersion: Gaussian Transport Model
Ground Deposition

## Slide 15: Atmospheric Dispersion: MACCS / HYSPLIT Model
Ground Deposition
Notes: Not a sample problem – but a animation for Fukushima using MACCS coupled with HYSPLIT
Also ground concentration, also Cs-137, map legend and units are different.

## Slide 16: Dosimetry: Exposure Pathways
Early Doses
Cloudshine
Groundshine
Direct inhalation
Resuspension inhalation
Skin deposition
Late Doses
Groundshine
Resuspension inhalation
Food ingestion
Water ingestion
Notes: MACCS does not model incidental soil ingestion, ingestion of food that comes from gardens or foraged in non-farm areas, or ingestion of fish or other aquatic food.
If users are interested in all calculated pathways, they first need to run both EARLY and CHRONC. Additionally, users need to consider the correct MACCS outputs.
Individual dose and cancer risk outputs do not include ingestion doses.
Population dose and health effect cases) provide are more complete measures of accident consequence.
Depends on your analysis. Late doses are not relevant to early health effects, for instance.

## Slide 17: Dosimetry: Dose Coefficients
The dose models use dose coefficients to convert from time-integrated air concentrations or ground concentrations to dose.
External pathways use a dose rate coefficient (e.g., Sv/s per Bq/m2)
Internal pathways (inhalation and ingestion) use an intake-to-dose coefficient (Sv/Bq)
Separate internal dose coefficients are provided for acute, lifetime, and annual doses

## Slide 18: Dosimetry: Types of Calculated Doses
Acute dose
  The portion of the dose that contributes to early health effects (i.e., accounts for the sparing effect)
  Includes only early-phase contributions to dose
  Uses a weighting factor (<1.0) to account for reduced risk associated with protracted internal doses from inhalation
Lifetime dose
  The dose that contributes to stochastic health effects (e.g., cancer)
  Includes both early-phase and late-phase contributions to dose
Annual dose
  The same as the lifetime dose, except annual doses are discretized into annual periods
  Includes both early-phase and late-phase contributions to dose

## Slide 19: Protective Actions
Protective actions reduce radiation exposures.
Protective actions are a tradeoff: They reduce radiogenic health effects but at a cost of other types of societal and economic impacts.
Many protective actions are dose-dependent
  If a projected dose exceeds a dose criterion during a specified exposure period, it triggers a protective action.
Notes: Projected dose: a dose assuming no protective actions
Certain portions of the population (e.g., outdoor workers) tend to have much less shielding than an average individual. To conservatively ensure that everyone is protected, protective action guides commonly use simplifying assumptions regarding shielding, such as assuming people are unprotected. Users should recognize that because of this, actual decisions for protective actions may be more extensive than what MACCS predicts.
Protective actions based on a dose rate (mSv/hr) rather than a projected dose (Sv) is not supported.

## Slide 20: Protective Actions
Early phase
  Evacuation and sheltering model
  Early relocation
  Potassium iodide ingestion
Intermediate phase
  Intermediate-phase relocation
Long-term phase
  Decontamination
  Non-farm areas: temporary and permanent relocation
  Farm areas: farming restrictions

## Slide 21: Protective Actions: Evacuation Transit and Routing
Two evacuation routing options
  Radial evacuation: Evacuees travel radially outward
  Network evacuation: Evacuees travel along user-specified grid
During transit, MACCS models evacuees as moving from spatial grid midpoint to midpoint in a stepwise fashion until they reach the travel boundary
Network evacuation direction with corresponding IDIREC values on a spatial grid.
Notes: Dosimetry uses a simplified tophat profile of the plume. Spatial element midpoints are inside the plume or they are not.
3 Travel phases: initial, middle, and late

## Slide 22: Protective Actions: Population Cohorts
User can divide the regional population into population cohorts that have similar characteristics during an emergency response
  Cohorts can have different protection factors, breathing rates, evacuation timelines, evacuation regions, and other factors.
  In the intermediate and long-term phases, MACCS treats all survivors as a single population cohort.
For each cohort, MACCS runs a separate simulation
Many outputs report both summary results from all cohorts and cohort-specific results
Notes: Cohorts can represent populations that:
evacuate early,
evacuate late,
refuse to evacuate,
those who evacuate from areas not under an evacuation order (i.e., a shadow evacuation), or
those who represent special groups such as schools, hospitals, or other institutions that may respond differently than the general public

## Slide 23: Protective Actions: Early Relocation
Early relocation is a dose-dependent response that occurs outside the evacuation and sheltering boundary (NUMEVA).
The projected relocation dose can be based on either the “TOTAL” or “AVOID” option. (New in MACCS v4.2)
  "TOTAL" evaluates the total dose from all air and ground concentrations and
  "AVOID" evaluates the avoidable dose from ground pathways.
  These new options are intended to mirror how decision-makers would evaluate doses during a radiological emergency using Turbo-FRMAC.
Early relocation has two areas, hotspot and normal relocation, and can have separate relocation times and dose criteria.
Once relocation occurs, displaced individuals receive no dose for the remainder of the early phase.
Notes: Early relocation, which can be thought of as a deferred evacuation, is an emergency response to displace individuals from at-risk areas outside the evacuation and sheltering boundary (NUMEVA).
Limitations:
Early relocation does not consider doses that may occur after the projection period.
The projection period assumes perfect knowledge of future plume segments

## Slide 24: Protective Actions: Long-term Phase
Land divided into farm and non-farm areas
Non-farm areas:
  Relocation occurs when projected dose exceeds any relocation criteria. (New in MACCS v4.2)
  Return / reoccupation occurs when decontamination is complete (if applicable).
  Condemnation occurs when decontamination is not feasible or cost effective.
Farm areas:
  Farming restrictions occur in farm areas when food ingestion doses exceed farmability criteria. (The farmability criteria depend on which food chain model the user selects.)
  Farming restrictions also occur when farmland exceeds relocation criteria, as MACCS assumes farmland is otherwise not farmable.
Decontamination:
  Decontamination occurs when projected dose exceeds relocation criteria (both farm and non-farm areas), but only when it can restore the area and is cost effective.
  A dose-dependent cleanup criterion allows users to model the acceptable cleanup level of contaminated areas. This allows users to model decontamination in lightly contaminated, habitable areas (non-farm area only). (New in MACCS v4.2)
Notes: When habitation restrictions are in place, people receive no doses (apart from worker doses during decontamination) and interdiction costs occur
Farm areas: There are two food ingestion models, those being the original MACCS food-chain model and the COMIDA2 food-chain model. Protective actions in farm areas depend on food chain model

## Slide 25: Protective Actions: Long-term Non-farm Areas
Doses Received After Long-term Protective Actions
Notes: Protective action levels for habitation restrictions can result in four possible outcomes:
land is immediately habitable, represented by the purple region,
land is habitable immediately after decontamination, represented by the blue and green regions,
land is habitable after decontamination and an additional period of interdiction, represented by the yellow region, and
land is condemned with removal and resettling of the population, represented by the red region.
Areas represented by the orange, green, and two blue areas can also become condemned if it is not cost effective to decontaminate. In this case, the dose in these areas is zero (the red line).

## Slide 26: Social And Economic Impacts
Nuclear accident impacts can broadly be divided into two categories: market and non-market
Market impacts (sometimes called “financial impacts” or “special damages”) include:
  Onsite and offsite property damage
  Economic disruptions
  Accident-related expenditures
Non-market impacts (sometimes called “noneconomic impacts” or “general damages”) include:
  Health effects
  Societal disruptions
  Environmental damage
Notes: Health effects fall into two categories: radiological and non-radiological health effects
Societal disruptions include:
Psychological distress – PTSD, depression, anxiety
Behavior and lifestyle changes – neglect for personal health, poor diet, and substance abuse
Loss of livelihood – displaced individuals lose their homes and jobs. Say they feel they have lost control of their lives, lose their sense of purpose
Dysfunction in families and communities – Displacement causes splits within families. Stigma towards evacuees. Disagreement about risk and compensation
Diminished standard of living - Displaced individuals tend to live in worse living conditions. In Japan, degraded living and social conditions from displacement created severe healthcare issues, particularly for the sick and elderly.
Environmental damage includes:
radiological effects
impacts from heavy decontamination / demolition

## Slide 27: Social And Economic Impacts
Evacuation and early phase relocation costs
Intermediate phase relocation costs
Long-term costs in non-farm areas ($/capita) and farm areas ($/farm hectare)
  Milk and crop disposal (farm areas only)
  One-time relocation (non-farm areas only)
  Decontamination
  Property depreciation
  Lost income
Two methods to calculate lost income
  “Loss of use” approach treats property as an investment based on a rate of return.
  “GDP-based” approach using the Regional Disruption Economic Impact Model (RDEIM) input-output model to calculate direct, indirect, and induced losses; and recovery gains.
Cost models do not consider
  Onsite damages or disruptions
  Property losses due to housing market impacts
  Certain expenditures (e.g., removal of condemned structures, cost of litigation and a compensation system, medical expenses)
  Economic disruptions due to stigma effects (e.g., tourism, trade)
  Non-market impacts
Notes: All modelled cost estimates are triggered based on a protective action.
MACCS does evaluate important metrics related to non-market impacts, including:
  the number of cancer fatalities and other health effects
  the number of displaced individuals
  the amount of land contamination

## Slide 28: Radiogenic Health Effects
Health effects from ionizing radiation are broadly categorized into two main categories:
  Stochastic effects, which include:
    Cancer incidence / fatality
    Heritable effects
  Tissue reactions (i.e., deterministic effects), which include:
    Early injury / fatality
    Degenerative conditions (i.e., cataracts, cardiovascular disease, and cerebrovascular disease).
MACCS analyses typically model cancer and early health effects.
Notes: MACCS analyses do not typically model heritable effects, but MACCS is capable of modeling them assuming heritable risk coefficients are available.
Scientific understanding of how best to model late effects of tissue reactions is still developing.

## Slide 29: Radiogenic Health Effects: Early Health Effects
MACCS estimates risk of early health effects (injury or fatality) using a dose response model based on a Weibull distribution.
The early health effect estimates use acute doses, which account for the sparing effect.
Early fatalities are estimated using a “pooled” risk model (i.e., the early fatality hazards are summed together)
Hematopoietic Syndrome Mortality Risks for Minimal Treatment, Supportive Treatment, and Mixed Treatment - Central Estimates for Exposure at High Dose Rate. (reproduced from Figure 3.1 of Evans 1989)
Notes: Early health effects have a sparing effect when doses are protracted over time.

## Slide 30: Radiogenic Health Effects: Cancer Incidence / Fatality
Four dose-response models are available in MACCS to calculate cancer incidence and fatalities:
  Linear, no threshold (LNT) with a dose and dose rate effectiveness factor (DDREF)
  Linear quadratic
  Annual threshold
  Piecewise linear
The linear no-threshold and the linear-quadratic models use lifetime doses.
The annual-threshold and piecewise-linear models use annual doses that exceed specified thresholds.

## Slide 31: Any Questions?
Instructions for requesting the MACCS code and MACCS-related documents can be found at: https://maccs.sandia.gov/
Supporting documents
  WinMACCS & MACCS User Guides
    MACCS User’s Guide and Reference Manual Report (SAND2023-01315)
    MACCS Theory Manual (SAND2021-11535)
  Technical Bases for Consequence Analyses Using MACCS (NUREG/CR-7270)
  MACCS-HYSPLIT Tools documentation
  Benchmark, verification and validation reports
  Complete set of published SOARCA reports

## Slide 33: MACCS Code Suite
MACCS:
  The main code of the MACCS code suite. MACCS assesses the public consequences associated with a hypothetical release of radioactive materials to the atmosphere, such as from a nuclear power plant accident.
  MACCS simulates the atmospheric dispersion, dosimetry, protective actions, health effects, and costs of a release.
WinMACCS:
  The graphical user interface for MACCS.
MelMACCS:
  An optional pre-processing code that creates a MACCS input file defining the atmospheric release (e.g., core inventory, release fractions, aerosol sizes, plume segment definitions).
  MelMACCS reads MELCOR output files and helps create an integrated accident progression and offsite consequence analysis.

## Slide 34: MACCS Code Suite (continued)
COMIDA2:
  An optional pre-preprocessing code that helps calculate anticipated food ingestion doses from farmland contamination via the food chain
MACCS-HYSPLIT Tools:
  An optional set of tools to generate a meteorological input file and / or to use the HYSPLIT atmospheric dispersion code (available from the US National Oceanic and Atmospheric Administration) in place of the original MACCS straight-line gaussian plume model.
LHS:
  An optional pre-processing code to help model uncertain input parameters by running Monte Carlo simulations of MACCS.
SecPop (US only):
  An optional pre-processing code that creates a site file using US Census information.
RDEIM (US only):
  An alternative economic consequence model that estimates the impact of a business disruption on the US gross domestic product considering interdependencies of US regional industries.

## Slide 35: MACCS Lineage
  Calculation of Reactor Accident Consequences (CRAC) Code (1975)
  Developed for the Reactor Safety Study (WASH-1400)
  CRAC2 (1982)
  Primarily used in 1982 siting study (NUREG/CR-2239)
  MACCS (MELCOR Accident Consequence Code System) (1990)
  Primarily used in NUREG-1150
  MACCS2 (1998)
  Developed to support DOE documented safety analyses of nuclear facilities
  WinMACCS/MACCS (2011)
  Enhance user friendliness
  Reduce likelihood of user errors
  Enable routine examination of uncertainty

## Slide 36: MACCS Utility Codes
MACCS/WinMACCS
  Current version is v4.2 (March 2023)
  Modernization efforts underway
MACCS-HYSPLIT tools
  Current version is v1.2 (March 2023)
SecPop
  Current version is v4.3.1 (July 2020)
  Planning to update with new US census data and programming language in late 2023
MelMACCS
  Current version is v4.0 (September 2022)
  Planning to update and release a new version early 2024
AniMACCS
  Current version is v1.3.1 (January 2022)

## Slide 37: MACCS 4.0 Improvements (06/2020)
Optional capability to perform high-fidelity atmospheric transport modeling with HYSPLIT (Lagrangian)
Optional state-of-practice, GDP-based model (RDEIM) to account for economic losses (database currently supports contiguous USA)
Support for special files needed by animation tool, AniMACCS
Limits extended on a large set of input parameters
Input parameters can be exported, including distribution definitions
Results for each weather trial are used to define quantile results

## Slide 38: MACCS 4.1 Improvements (07/2021)
Near-field modeling improvements:
  Comparison of several near-field atmospheric transport and dispersion codes including QUIC, ARCON96, and AERMOD concluded MACCS provides a conservatively bounding assessment in the near-field
  MACCS v4.1 enhancements added for plume meander and trapping and downwash to simulate or bound near-field assessments of other codes
New projective peak dose output option
Documentation added to help menu in WinMACCS
Updates to the RDEIM economic model
Mixing layer information for each time period
Time synchronization between local time and UTC
Pop-up window for converting previous version
Linux version of MACCS 4.1

## Slide 39: MACCS 4.0/4.1 Licensing Process
MACCS 4.0/4.1 contains new licensing features
  Software is locked to a specific computer
  Licenses are for one-year duration
Steps to activate license
  Run WinMACCS 4.X.0 Setup.exe (no installation key required)
  Open WinMACCS 4.X.0
    A popup screen briefly describes the licensing process
    Readme file provides more details on licensing process
  Run CreateLicenseRequestFile.exe in folder C:\Users\Public\WinMACCS to create license.request
  Send a copy of license.request to wg-maccs-entity@sandia.gov
  Once approved, Sandia sends product.key to user
  License key is linked to WinMACCS

## Slide 40: MACCS 4.2 Improvements (03/2023)
Remove node locking from license
  Only time limit for licenses
  Removes three steps from process
  License included in 4.2 installer expires March 2024, new one to be issued before then
Up to 999 radionuclides
  Still limited to six member decay chain length
  Need dose coefficient data for radionuclides
Split indirect costs in economic model
Dual dose criteria
Relocation dose projection and timing
Decontamination in habitable areas
Skin pathway standardization

## Slide 41: Recent MACCS Development
MACCS 4.0 was released in June 2020
  HYSPLIT capability added
  RDEIM economic model added
  AniMACCS capability added
MACCS 4.1 was released in July 2021
  Nearfield updates for plume meander models
MelMACCS 4.0 was released September 2022
MACCS 4.2 was released March 2023
  Updates to projected dose calculations for protective actions
  Addition of a cleanup criterion
  Increase in maximum number of radionuclides
  Additional output for RDIEM (economic model)
MACCS modernization underway!

## Slide 42: MACCS Modernization
Working collaboratively with the US NRC to determine the future vision for MACCS
  Effectively tackle the consequence analysis challenges of the future
  Incorporate modern programming languages and techniques
  Be compatible with modern computing platforms
  Increased flexibly and modularity
  Support advanced reactor consequence analysis and future model updates
Divided into two main efforts
  User Interface (WinMACCS)
  Analysis code (MACCS)

## Slide 43: User Interface Modernization
Visual Basic 6 no longer supported
  Java, JavaScript and other modern tools
MACCS-UI to have the same functionality as current WinMACCS
  Ability to add more capabilities in the future
Same interface with MACCS
  Atmos.inp, Early.inp, Chronc.inp
  Model1.out, Model1.bin
  Import previous WinMACCS 4.x projects

## Slide 44: Analysis Code Modernization
Goals and benefits
  Maintain backwards compatibility
  Compatible with what users currently use
    MACCS UI
    Command line
  Better readability and easier modification of code
  Improve and modify input functionality
  Increase output capabilities
  Work to support potential improvements and model capabilities
Modern programming practices will be used for enhanced readability and modification of MACCS code
  Convert mix of Fortran 77 & 90+ portions of code to modern Fortran
  Clean up memory use by using dynamic memory
  Modularize to facilitate adding or replacing models
Implement such that MACCS remains in a release-ready state

## Slide 45: Auxiliary and Supporting Files
Dose coefficient (DCF) files for LNT and non-LNT applications
  FGR-13 (based on FGR-13 using standard radiation weighting factors)
  FGR-13 Gray Equivalent (Rev. A) (based on FGR-13 using relative biological effectiveness (RBE) factors consistent with FGR-13 cancer induction modeling and with all SOARCA analyses)
  Updated versions accompany MACCS 4.2
COMIDA2 files to go with each type of dose coefficient file
  Exposure duration (LASTACUM) set to 50 years
NRC and DOE sample problems
Tutorials based on NRC sample problems
Fogbugz used for problem reporting and corrective actions – https://ersdt.fogbugz.com/

## Slide 46: References
CRAC / MACCS Research Projects:
  WASH-1400, NUREG-75/014, “An Assessment of Accident Risks in U. S. Commercial Nuclear Power plants,” U.S. Nuclear Regulatory Commission, Washington, DC, 1975.
  NUREG/CR-2239, “Technical Guidance for Siting Criteria Development,” U.S. Nuclear Regulatory Commission, Washington, DC, December 1981.
  NUREG-1150, Vol. 1, “Severe Accident Risks: An Assessment for Five U.S. Nuclear Power Plants,” U.S. Nuclear Regulatory Commission, Washington, DC, 1990.
  NUREG/CR-7110, Vol. 1, Rev. 1, “State-of-the-Art Reactor Consequence Analyses Project Volume 1: Peach Bottom Integrated Analysis,” U.S. Nuclear Regulatory Commission, Washington DC, 2013.
  NUREG/CR-7110, Vol. 2, Rev. 1, “State-of-the-Art Reactor Consequence Analyses Project Volume 2: Surry Integrated Analysis,” U.S. Nuclear Regulatory Commission, Washington DC, 2013.
  NUREG/CR-7245, “State-of-the-Art Reactor Consequence Analyses (SOARCA) Project Sequoyah Integrated Deterministic and Uncertainty Analyses,” U.S. Nuclear Regulatory Commission, Washington, DC, 2019.
  Draft NUREG, “U.S. NRC Level 3 Probabilistic Risk Assessment (PRA) Project, Volume 3d: Reactor, At-Power, Level 3 PRA for Internal Events and Floods, Draft for Comment,” U.S. Nuclear Regulatory Commission, Washington DC, 2022. ADAMS Accession No. ML22067A215.
MACCS Code Manuals:
  SAND2021-11535, “MACCS Theory Manual,” Sandia National Laboratories, Albuquerque, NM, 2021.
  SAND2022-7112, “MACCS (MELCOR Accident Consequence Code System) User Guide – Version 4.0, Revision 1,” Sandia National Laboratories, Albuquerque, NM, 2022.
Emergency Preparedness Reports:
  NUREG-0396, EPA 520/1-78-016, “Planning Basis for the Development of State and Local Government Radiological Emergency Response Plans in Support of Light Water Nuclear Power Plants,” U.S. Nuclear Regulatory Commission, Washington, DC, December 1978. ADAMS Accession No. ML051390356
  NUREG-0654, Rev. 1, Supplement 3, “Criteria for Preparation and Evaluation of Radiological Emergency Response Plans and Preparedness in Support of Nuclear Power Plants: Guidance for Protective Action Strategies,” U.S. Nuclear Regulatory Commission, Washington, DC, November 2011.
MACCS Applications Supporting Emergency Preparedness:
  NUREG/CR-6953, Vol. 1, SAND2007-5448P, “Review of NUREG-0654, Supplement 3, ‘Criteria for Protective Action Recommendations for Severe Accidents’,” U.S. Nuclear Regulatory Commission, Washington, DC, 2007.
  NUREG/CR-6953, Vol. 3, SAND2010-2806P, “Review of NUREG-0654, Supplement 3, ‘Criteria for Protective Action Recommendations for Severe Accidents’,” U.S. Nuclear Regulatory Commission, Washington, DC, 2010.
  SAND2022-3706, “Scoping Analysis of MACCS Modeling Improvements for the Study of Protective Action Recommendations,” Sandia National Laboratories, Albuquerque, NM, 2022.