## Slide 1: RASCAL Beginner Training
Sam Hanson, PhD
January 27, 2026
0930-1200 ET

## Slide 2: RASCAL Team
RAMP
U.S. NRC Office of Regulatory Research (RES)
RASCAL Primary User
U.S. NRC Office of Nuclear Security and Incident Response (NSIR)
Rigel Flora
Health Physicist, RASCAL Project Manager
Sam Edwards
Computer Scientist
Stephanie Bush-Goddard, PhD
RAMP Manager
Sam Hanson, PhD
Health Physicist

## Slide 3: Training and support at ramp.nrc-gateway.gov
Need Account to Access
  Non-Disclosure Agreement (NDA)
  Fed/State/Local/International/Private
Code Distribution
Technical Support
  Technical documentation (NUREGs)
  Training
  FAQs & Forums

## Slide 4: RASCAL Resources
NUREG-1887 for RASCAL 3
NUREG-1940 for RASCAL 4
NUREG-1465 for LOCA
SOARCA for SBO
Aviationweather.gov for meteorology (U.S.)

## Slide 5: RASCAL Slide
Every time we ask you to use RASCAL, you’ll see one of these blue slides.
It will include information needed to complete the steps.

## Slide 6: Technology Review
Nuclear Power Plant
Spent Fuel
Fuel Cycle
Other Material

## Slide 7: Reactor Types
Core inside reactor vessel creates heat, steam is created (main loop in BWR, secondary loop in PWR), steam turns turbine, which produces electricity
Pressurized Water Reactor (PWR)
Boiling Water Reactor (BWR)

## Slide 8: Large releases will come from major fuel damage, only caused from lack of cooling
No heat removal leads to fuel cladding failure and fuel melt
Eventual RCS overpressure / leakage
Possible containment overpressure / leakage
Defense in Depth
Notes: Defense In Depth

## Slide 9: Spent Fuel
Every 12-24 months, a fraction of reactor core is replaced and moved to a pool to cool.
5-10 years later, cooler fuel moved to dry cask

## Slide 10: Fuel Cycle
Fuel cycle facilities convert, enrich, and fabricate mined material into reactor fuel
RASCAL Supports these accident types:
  UF6 Cylinders
  Criticality
  Fire/Explosions involving Uranium Oxide

## Slide 11: There are 4 primary tools and 3 additional tools on the RASCAL Home Page.

## Slide 12: Where does RASCAL fit in the phases of a radiological emergency?
Pre-release
Plume (early)
Intermediate
Ingestion
RASCAL (STDose)
RASCAL (FMDose)
Turbo FRMAC

## Slide 13: Our Training Will Focus on STDose
Source Term to Dose module creates an atmospheric source term, processes weather data, and calculates doses
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 14: RASCAL Defines Atmospheric Source Term
Determines radionuclides available for release
  May be single nuclide or complex core damage
  Time-dependent isotopes and activity
Source material may be filtered, reduced, or decayed
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 15: Result is Radionuclides Released to Environment Over Time (Atmospheric Source Term)
Isotopic activity over time (15 min)
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 16: Atmospheric Source Term is Moved using ATD Models
Atmospheric Transport and Dispersion Models
  Transport material based on weather conditions
  Track material to where it falls/washes on ground
  Accounts for dry/wet processes and particle size
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 17: Final Calculations Provide Doses and Concentrations over Calculation Area
Dose calculation accounts for multiple pathways
  External (Groundshine + cloudshine)
  Internal (Inhalation + ingestion)
Results includes other display/calculation options
Wind
Generation of Source Material
Plume
Dose/Concentration
Atmospheric Source Term

## Slide 18: Walkthrough
Let’s step through a RASCAL run together
  Watch our discussion slides without using your RASCAL (screenshots may not match)
  At each blue slide, you will input information into RASCAL

## Slide 19: Select STDose
Most of what you will be using RASCAL for (dose assessment) will be done with Source Term to Dose (STDose).

## Slide 20: Using STDose
Input information on the buttons on left, from top to bottom
  Meteorology can be input once a location is selected
Translate available data into RASCAL inputs
  Some data is “static”; enter once
  Some data is “dynamic” and changes with time as more communications are established and as conditions evolve

## Slide 21: Start by Clicking Event Type
RASCAL breaks up locations and models into 4 types:
  NPP
  Spent Fuel
  Fuel Cycle
  Other/Materials

## Slide 22: Next, Click Event Location
Select from a list of predefined sites
  All U.S. facilities (NPPs, Fuel Cycle, Materials)
  International NPPs including: Mexico, South Africa, Taiwan, and UAE
Or, define a custom site
  Need Latitude/Longitude coordinates
  Does not build in roughness or topography

## Slide 23: At the Bottom of Location, Check Reactor Power
Units of megawatts thermal (MWt) and is a direct measure of the energy produced by fission. This number is used by the model to determine the fission product inventory in the core.
The facility database contains the power level at which the reactor is allowed to operate.
Since reactors generally try to operate at 100% power, this value should rarely be changed.

## Slide 24: Also Check Burnup
Fuel burnup has units of megawatt-days per metric ton of uranium (MWd/MTU) and is a measure of how much fission energy has been produced by the fuel elements that are currently in the core.
RASCAL uses burnup to adjust core inventory for long-lived radionuclides in the core fuel. A mid-life core value is used as default instead of site-specific values
If you have a burnup value – use it, otherwise the default is OK.

## Slide 25: Your Turn to Use RASCAL
Start the RASCAL program & select STDose
Click Event Type
  Select Nuclear Power Plant
  Click OK
Click Event Location
  Select Beaver Valley, Unit 1
  Click OK

## Slide 26: Let’s walk through together

## Slide 27: Knowledge Check
The RASCAL STDose model supports which of the following radiological emergency phases? [select all that apply]
  Pre-release
  Plume (early)
  Intermediate
  Ingestion
T or F, RASCAL can model releases from sites not in its facility database?
  True
  False

## Slide 28: Source Term
Source term models calculate material that can be released
Pick the best model; may have multiple options
Available choices depend on Event Type
Nuclear Power Plant
Spent Fuel
Fuel Cycle
Other Materials

## Slide 29: Nuclear Power Plant
RASCAL has 9 nuclear power plant source term options:
4 based on reactor condition models
5 based on nuclide measurements

## Slide 30: Nuclear Power Plant
Long Term Station Blackout
Without onsite & offsite AC power and other cooling methods, could lead to core melt
User inputs event timing

## Slide 31: Nuclear Power Plant
Loss of Coolant Accident (LOCA)
Loss of reactor coolant, leads to core uncovery and fuel melt
User inputs event timing

## Slide 32: Nuclear Power Plant
Coolant Release Accident
Loss of reactor coolant where only coolant is released, no core melt expected
Very small releases

## Slide 33: Nuclear Power Plant
Containment Radiation Monitor
Estimates core damage based on containment rad monitor

## Slide 34: Nuclear Power Plant
Coolant or Containment Air Sample
User inputs entire source term by nuclide
RASCAL does not extrapolate source term from subset of nuclides
Not expected to have data during event

## Slide 35: Nuclear Power Plant
Effluent Releases - Mixtures
User inputs activity rates of:
  Noble Gas
  Iodines
  Particulates
RASCAL fractionates by nuclide based on core inventory
Often based on utility conversion or calculation

## Slide 36: Nuclear Power Plant
Effluent Release Rates/Concentration
User inputs entire atmospheric source term by nuclide
RASCAL does not extrapolate source term from subset of nuclides
Can be used to manually define source term, including small/custom releases

## Slide 37: Source Term
Source term models calculate material that can be released
Pick the best model; may have multiple options
Available choices depend on Event Type
Nuclear Power Plant
Spent Fuel
Fuel Cycle
Other Materials

## Slide 38: Spent Fuel
For Spent Fuel, RASCAL has 3 source term options
Includes both pool and dry storage
Sites are collocated with NPPs

## Slide 39: Spent Fuel
Pool - Uncovered Fuel
Models clad/zirconium fire whether possible or not
User inputs fuel pool inventory and fire start/end times

## Slide 40: Spent Fuel
Pool - Damaged Underwater
For fuel handling accidents
Very small releases
User inputs amount of fuel damaged

## Slide 41: Spent Fuel
Dry - Cask Release
4 damage options
Small to zero release
User defines inventory of fuel and damage type

## Slide 42: Source Term
Source term models calculate material that can be released
Pick the best model; may have multiple options
Available choices depend on Event Type
Nuclear Power Plant
Spent Fuel
Fuel Cycle
Other Materials

## Slide 43: Fuel Cycle
RASCAL can model certain events from fuel fabrication facilities
  UF6 chemical models
  Criticality
  UO2 Fire/Explosion

## Slide 44: Fuel Cycle
UF6 Release from Cylinder
Gaseous UF6 released
Special plume model with chemical conversion process
More chemically dangerous than radiological

## Slide 45: Fuel Cycle
Fire or Explosion involving Uranium Oxide
Small amounts of material put into atmosphere from event
User inputs material at risk and release fractions / rates

## Slide 46: Fuel Cycle
Criticality
Mainly focused on direct shine from criticality event
  Very small amount of activated material put into atmosphere

## Slide 47: Fuel Cycle
Effluent Release Rates/Concentration
User inputs entire atmospheric source term by nuclide
RASCAL does not extrapolate source term from subset of nuclides
Can be used to manually define source term, including small/custom releases

## Slide 48: Source Term
Source term models calculate material that can be released
Pick the best model; may have multiple options
Available choices depend on Event Type
Nuclear Power Plant
Spent Fuel
Fuel Cycle
Other Materials

## Slide 49: Other Materials Locations
RASCAL also has 3 “other” materials options
Useful for modeling transportation accidents, lab accidents, etc.
All models still focus on atmospheric releases
  Liquid releases (like spills and leaks) are not modeled in RASCAL

## Slide 50: Other Materials Locations
Effluent Release Rates/Concentration
User inputs entire atmospheric source term by nuclide
RASCAL does not extrapolate source term from subset of nuclides
Can be used to manually define source term, including small/custom releases

## Slide 51: Other Materials Locations
Sources and Material in a Fire
Small amounts of material put into atmosphere from a fire
User inputs material at risk and release fractions / rates

## Slide 52: Source Term
Source term models calculate material that can be released
Pick the best model; may have multiple options
Available choices depend on Event Type
Nuclear Power Plant
Spent Fuel
Fuel Cycle
Other Materials

## Slide 53: Pick a Source Term
For this scenario, the most appropriate model would be the LOCA model

## Slide 54: Enter Source Term Details
Each model requires additional details like timing or measurements
For the LOCA model:
  Time of reactor shutdown
    Starts the decay of all nuclides in the core (they’re in equilibrium before)
  Time core was uncovered
    When NUREG-1465 models start, starting with 30 min of gap activity, then fuel melt
  Is the core recovered?
    Additional material stops being generated after the core becomes recovered
All times entered with 24-hour clock

## Slide 55: Your Turn to Use RASCAL
Click Source Term
Select Loss of Coolant Accident (LOCA)
  Click OK
Input timing sequence numbers
  Shutdown Time - 0800
  Time of Core Uncovery – 1030
  Select Yes for Core Recovered, Time – 1300
  Click OK

## Slide 56: Let’s walk through together

## Slide 57: Knowledge Check
Why is it important to enter the reactor shutdown time?
  That is when the radionuclide decay calculation starts
  That is when the release starts
  That is when the damage to the reactor fuel begins
If the core is recovered, will there still be a release to the atmosphere?
  Maybe, it depends on the release pathway and leak rate
  Yes, that just stops further damage to the core
  No

## Slide 58: As you can see, the Case Summary tab updates as information is added
As each step is completed, the input information is added to the case summary displayed.

## Slide 59: Now We’ll look at Release Pathway
RASCAL needs information on how generated material is released to the atmosphere
  Pathway
  Height
    Wind speeds change with height
  Reduction
    Amount of material reduced by decay, holdup, filter, sprays
  Timing
    Release rates, start and stop
We’ll start by selecting the Pathway

## Slide 60: For this Release Pathway option, We’ll need to input:
Release Height
  10m is minimum height allowed (ground release)
Select leak rate type
  Percent Volume / Time (e.g., 3%/hour)
  Containment pressure / Hole Size (e.g., 30 psi/2 cm2)
Define release timeline
  Used for leak rate and additional conditions
  Need to review/set initial conditions, then can add rows as needed
Don’t copy this data. For discussion purposes only.

## Slide 61: Your Turn to Use RASCAL
Click Release Path
Select Containment leakage/failure, Click OK
Ensure release height is set to 10m
Change the initial leak rate (at 10:30) to 5% / day
Keep sprays off
Add row and enter
  Time: 18:00 Event Type = Leak rate Setting = 0.0 %/d
Click OK

## Slide 62: Let’s walk through together

## Slide 63: Knowledge Check
For a LOCA accident, RASCAL can model the release of material to the atmosphere through which of the following pathways? [select all that apply]
  Containment
  Steam generator
  Bypass of containment via other systems
  Direct from the reactor vessel
T or F, in RASCAL a release height of 10m is considered ground level?
  True
  False

## Slide 64: Moving onto Meteorology
Actual
  Enter station observations/forecasts
  Manual entry or internet download
Pre-defined (non site-specific)
  Simple static weather conditions
  Easy/fast if no meteorological data known, but doesn’t include topo/roughness
Predefined (site-specific)
  Allows custom creation of likely conditions

## Slide 65: We’ll Mostly Use Actual for Exercises/Events
We won’t use pre-defined except in training
For actual conditions, weather data is managed as site-dependent files
  Create New / Edit
  View any previously saved weather files
  Usable as long as times support scenario

## Slide 66: Each Site contains predefined weather stations
Table and map show site and surrounding weather stations
Select stations with plume direction in mind

## Slide 67: Inputting Weather Data
Select weather station on the left to input its data on the right:
  Type
  Date/Time
  Wind Direction/Speed
  Stability
  Precipitation

## Slide 68: RASCAL uses observed and/or forecast weather data
RASCAL can model releases in the past (all observations), in the future (all forecasts), or that span both.
Current Time
Observations
Forecasts
Release 1
Release 2
Release 3

## Slide 69: RASCAL Can Run with a Single Weather Datapoint
However, the initial meteorological data must fall within 2 hours before the start of the release to the atmosphere. (Release starts at 10:30; must have some meteorology defined within the 8:30 to 10:30 window)
Release 1
Release 2
Release 3
2 hours

## Slide 70: Although Single Datapoint Weather is possible, More Data is Preferred
Important when the release may start in the future or may continue for some period of time. You will likely need both observed and forecast data.
However, our scenario doesn’t have additional info like forecasts yet.
Release 1
Release 2

## Slide 71: Process Data
Click Process Data to compile all the weather data into a form that the models can use.

## Slide 72: RASCAL processes all entered data into a merged gridded field that changes over time
This named file will show on the main met screen
Weather details can be viewed if needed (View dataset)

## Slide 73: Finally, Select Which Weather File You Want RASCAL to Use
RASCAL will return to the main Meteorology screen
Highlight the desired weather data

## Slide 74: Your Turn to Use RASCAL
Click Meteorology
Select option for Actual Observations and Forecasts
  Click Create New button
Click Enter Data button
For the BEAV station enter the following:
  Time = 10:00
  Winds = from 45 deg at 2 mph
  Stability class = B
  Precipitation = None
  Click OK
Click Process Data button then click OK
Click the Return button
Make sure your newly created file is selected in blue in the list of available datasets. Click OK

## Slide 75: Let’s walk through together

## Slide 76: Knowledge Check
T or F, pre-defined weather conditions are acceptable to use in a real event?
  True
  False
T or F, RASCAL requires at least some weather data to drive the ATD models?
  True
  False
T or F, RASCAL allows you to enter weather data that varies in both space and time?
  True
  False
T or F, RASCAL can model a release that may occur in the future?
  True
  False

## Slide 77: Calculate Doses
Nothing has been calculated at this point
With a few additional parameters, RASCAL will perform all its calculations

## Slide 78: Pick a distance to set the calculation area
Shorter distances provide higher resolution
Rule of Thumb – start on the 10 mile distance. If doses are high at the 10 mile edge, go to 25 miles

## Slide 79: Closer calc distances provide better resolution if you don’t need to see further out
10 mile grid – cells are .5 mile wide
100 mile grid – cells are 5 miles wide

## Slide 80: Define a Calculation Time
Duration after the first release to atmosphere that RASCAL terminates the release, plume movement and dose calculations
If time is set too short, dose may be missed; no disadvantage to going long (except runtime)

## Slide 81: Set calculation duration to allow for trailing plume edge to reach set distance
Leading Edge, released at t=0.
Trailing edge, released at t=8.
Wind speed determines when trailing edge reaches 10 miles
10 mi
10 mi

## Slide 82: There is a rule-of-thumb for estimating the calculation duration
10 mi
For our problem, 7.5 hr release with 2 mph winds, calculate a duration for a 10-mile grid.
7.5 hours + (10 miles / 2 mph) = 12.5 hours
Add 10% to get 13.75, then round up to the nearest hour (14)
“Release Duration”
Calculation Distance

## Slide 83: Select the inhalation dose coefficients to be used
ICRP 26/30 vs 60/72
Currently, NRC and most States use 26/30
New EPA PAG Manual uses 60/72
Differences are inclusion of child thyroid CEDE and some minor dose values changes

## Slide 84: Enter the case information
RASCAL requires a case title
Description used for justification or special notes; don’t need to repeat case info
Select and/or define an analyst name

## Slide 85: What happens when the OK button is clicked?
RASCAL calculates the atmospheric source term and runs the ATD models with the given weather
  You cannot interrupt the calculations
Once complete, view results tabs at the bottom
  Case Summary
  Source Term
  Maximum Dose Values

## Slide 86: Your Turn to Use RASCAL
Click Calculate Doses
Leave Distance of Calculation at 10 miles
Set End Calculations at:
  Start of release to atmosphere plus: 14h
Click OK to start the calculations

## Slide 87: Let’s walk through together

## Slide 88: Knowledge Check
Which calculation grid has the better resolution?
  50-mile
  10-mile
  They have the same resolution
What would you set as the calculation duration with a 7-hour release with 5 mph winds on a 10-mile grid?
  8 hours (RASCAL default)
  9 hours
  10 hours or more
  96 hours (RASCAL max)

## Slide 89: RASCAL Results
When RASCAL is finished calculating, it shows this screen, which is just 1 of 3 tabs at the bottom
They each contain different information and have a different purpose, let’s go through them
Your results will be different than screenshot. For discussion purposes only.

## Slide 90: Case Summary Tab Shows Inputs
The Case Summary tab has been populating as we added info
You can use it as a great way to check your inputs all at once or compare inputs against other dose assessors
Your results will be different than screenshot. For discussion purposes only.

## Slide 91: Source Term Tab Shows Details for Release to Atmosphere
Summary window
View Balance
  Where nuclides are at the end of the simulation
View Importance
  What nuclides are contributing the most to dose
Release vs. Time
  Displays amount of each nuclide released each 15 minute time step
  Can be exported
Your results will be different than screenshot. For discussion purposes only.

## Slide 92: Max Values Table Shows dose snapshot
Summary window
  Doses important for protective actions (TEDE, Thyroid)
  Underlines doses exceeding PAGs
Select distance
  Close in vs selected “far out” model distance
Does not show direction
Your results will be different than screenshot. For discussion purposes only.

## Slide 93: For Additional Result Information, Click Detailed Results
Provides additional graphical and tabular outputs
Result types at top
  Dose-related
  Deposition/Measurements
  Acute doses
Settings on the bottom
  Time - cumulative or rate
  Map/Table; Close-in or Further Out
  Units

## Slide 94: Difference between Footprint and Table
Footprint provides celled results on map
Table provides numeric values
Both can be exported, map can be queried, table can be filtered
Footprint
Table

## Slide 95: Difference between “close in” and “Far Out”
Plume Model
Puff Model
Two ATD models are used in the calculations
  Resolution advantages
  Overlap may not line up exactly

## Slide 96: Your Turn to Use RASCAL
Examine the results
  Maximum Dose Values tab shows some doses at selected distances
  Source Term tab show details about the atmospheric release
  Click Details Results to see options for looking at dose on a map

## Slide 97: Let’s walk through together

## Slide 98: Knowledge Check
What is the projected TEDE (rem) at 5 miles?
  1.4E+00
  1.7E+00
  3.2E+01
  None of the above values
What percentage of the release to the atmosphere is iodines?
  0.6%
  12.9%
  16.4%
  None of the above values
What direction is the plume projected to travel?
  Northeast
  East
  Southeast
  Southwest

## Slide 99: This concludes our intro walkthrough
You should now be able to click through RASCAL start to finish.
Remember that resources & training can be found at: https://ramp.nrc-gateway.gov/

## Slide 100: Available topics for future
Nuclear Power Plant Accidents
  Long-Term Station Blackout
  Monitored Effluent Mixtures
  Containment Rad Monitor
  Steam Generator Tube Rupture
Other Radiological Accidents
  Spent Fuel Pool
  Fuel Cycle
  Other Materials Accident
  Transportation Accident
RASCAL features
  Multi-Unit Assessment
  Comparing with Field Measurements
  Field Team Dosimetry & DRDs
  Download Met from Internet (MetFetch)
  Special Receptors